## Slide 1: Sprayer Nozzles and Droplet Size
Eric P. Prostko
Professor & Extension Weed Specialist
Dept. of Crop & Soil Sciences
ANR Training
November 2019

## Slide 2: Coverage vs. Drift Control (It’s all about droplet size)
Larger (coarser) Drops
  Less coverage but better drift control
Smaller (finer) Drops
  Better coverage but less drift control
Coverage is pesticide dependent
  Contact = smaller drops
    Liberty, Gramoxone
  Systemic = larger drops
    Roundup, 2,4-D, dicamba

## Slide 3: Droplet Size
Goal = larger droplets; eliminating fines
micron (µm) is a unit of measure equivalent to 1/25,000 of an inch.
Notes: You must understand spray droplet size if you are going to be successful. Micron is a word that sounds complex but it really isn’t as it is simply a measure of the droplet size. This chart provides you with a few comparisons to make you more comfortable with the terminology. For example a 100 micron droplet is the size of human hair where a 400 micron droplet is the size of a staple. In the past with products like Liberty a 300 micron droplet was ideal because it works like a contact herbicide where you have to help out by getting throughout coverage of the herbicide on the weed. Now with dicamba and 2,4-D, being systemic, you still have to get them on the weed but they can do a lot of the work themselves by moving throughout the plant so a larger droplet is a better choice (green arrow). Now why do we want a larger droplet.

## Slide 4: Volume Median Diameter (VMD)
value where 50% of the total volume or mass of liquid sprayed is made up of droplets larger than this value, and 50% is made up of droplets smaller than this value.
Dv0.5
Measured in microns

## Slide 5: Spray Tip Classification by Droplet Size
Category | Symbol | Color Code | Approximate VMD2 (Microns)
Extremely Fine | XF | PURPLE | < 60
Very Fine | VF | RED | 61-105
Fine | F | ORANGE | 106-235
Medium | M | YELLOW | 236-340
Coarse | C | BLUE | 341-403
Very Coarse | VC | GREEN | 404-502
Extremely Coarse | XC | WHITE | 503-665
Ultra Coarse | UC | BLACK | >665
1Estimated from sample reference graph in ASBAE/ANSI/ASAE Standard S572.1
2VMD = Volume median diameter

## Slide 6
Chart: 
Series 1 | 188 | 128 | 68
Series 2
Series 3
Series 4
Series 5
Series 6
Series 7
Distance of Visual Dicamba Damage from Drift in Cotton. Moultrie GA. 2018.
188 feet
128 feet
68 feet
Medium
(236-340)
Course
(341-403)
Ultra Course
(>665)
Droplet Size (µm)
Notes: I want to stress even with the right tip it is not zero. In fact one of our greatest concerns, is that you guys think all you need is to get the right tip and you are bullet proof.

## Slide 7
11002DG
VMD50 = 322 (M)
AIXR 11002
VMD50 = 402 (C)
TTI 02
VMD50 = 524 (XC)
VMD for common nozzle types

## Slide 9: You Can Put More than 1 Nozzle on a Boom

## Slide 10: What Nozzles Do I Like?

## Slide 11: Other Common Nozzle Questions
How much do they cost (2019)?
  TTI-11004-VP-CE = $9.86
  XRC-11004-VP = $2.96
How long do they last?
  How many acres? What was sprayed? What are they made of? (brass, stainless steel, polymer, ceramic)
  Replace when flow exceeds 10% of new nozzle

## Slide 12: Nozzle Requirements for Auxins (tolerant cotton and soybeans)
Xtendimax®
Enlist One™

## Slide 13: How do “auxin” nozzles work in real world?
Henley Farm, Miller County, April 10, 2017

## Slide 14: 2017/2018/2019 Nozzle Tests VMD50 and Coverage
R1
R2
R3
10 feet
10 feet
tractor

## Slide 15: Commercial Sprayer Nozzle Tests - 2019
Patterson Farm, Worth County, April 4, 2019
JD4730, 90’ boom, 20” nozzle spacing, 12.5 MPH, 20 GPA, 42-57 PSI

## Slide 16: Worth County Nozzle Test April 4, 2019 (Rep 2, card #2)
JD 4730, 90’ boom, 20” spacing, 20 GPA, 12.5 MPH, 42-57 PSI, 36” boom height
XRC-11006
TTI-11006

## Slide 17: Commercial Sprayer Nozzle Tests - 2019
Sikes Farm, Bulloch County, March 21, 2019
JD4630, 90’ boom, 15” nozzle spacing, 11.6 MPH, 12 GPA, 18-20 PSI

## Slide 18: Bulloch County Nozzle Test March 21, 2019 (Rep 2, card #4)
JD 4630, 90’ boom, 15” spacing, 12 GPA, 12 MPH, 28 PSI, 36” boom height (avg.)
XRC-11004
TTI-11004
TDXL-11004D

## Slide 19: Commercial Sprayer Nozzle Tests - 2019
Waters Farm, Pierce County, March 26, 2019
JD4730, 100’ boom, 15” nozzle spacing, 11.6 MPH, 15 GPA, 18-20 PSI

## Slide 20: Pierce County Nozzle Test March 26, 2019 (Rep 1, card #5)
JD 4730, 100’ boom, 15” spacing, 15 GPA, 11.6 MPH, 18-20 PSI, 36” boom height (avg.)
XR-11006
TTI-11006

## Slide 21: Droplet Size and Spray Coverage from 2019 Nozzle Tests with Commercial Sprayers
 | Bulloch1,3 |  |  | Pierce1,4 |  | Worth2,5 | 
 | TTI- 11004 | XRC- 11004 | TDXL- 11004 | TTI- 11006 | XR- 11006 | TTI- 11006 | XRC-11006
VMD50 (microns) | 456 a6 | 182 b | 411 a | 381 a | 196 b | 481 a | 348 b
Coverage (%) | 11.8 a | 8.1 b | 12.0 a | 5.3 a | 3.4 b | 10.0 a | 7.4 a
1According to DepositScan
2According to DropletScan
3JD4630, 90’ boom, 15” nozzle spacing, 12.0 MPH, 12 GPA, 28 PSI, 36” boom height
4JD4730, 100’ boom, 15” nozzle spacing, 11.6 MPH, 15 GPA, 18-20 PSI, 36” boom height
5JD4730, 90’ boom, 20” nozzle spacing, 12.5 MPH, 20 GPA, 42-57 PSI, 36” boom height
6Means in the same row within same location with the same letter are not significantly different (THSD 0.10).
Means from 21 kromekote water sensitive cards.

## Slide 22: 2019 Nozzle Tests (Weeds, Insects, Disease, Yield)

## Slide 23: 2019 Peanut Nozzle Tests
County | Rotation | Variety | Irrigated (I) or Dryland (D) | Tillage | Row Pattern | Planting Date | Digging Date | Harvest Date
Bulloch | cotton cotton peanut | GA-06G | D | ST | Single | May 17 | Oct. 3 | Oct. 8
Pierce | cotton cotton peanut | GA-06G | D | CT | Single | May 18 | Oct.1 | Oct. 5
Worth | peanut cotton peanut | GA-06G | I | CT | Twin | May 9 | Sept. 21 | Sept. 24

## Slide 24: 2019 Nozzle Tests Pesticides/Fertilizers Applied
County | Total Applications (#) | Herbicides | Fungicides | Insecticides | Other
Bulloch | 6 | Valor Strongarm Cadre Dual Magnum 2,4-DB | Approach Prima Equus Elatus Convoy Tebusol | Dimilin | Boron PegPower
Pierce | 6 | Valor Dual Magnum Cadre 2,4-DB | Bravo Priaxor Provost Silver Tebuconazole | Dimilin | Boron
Worth | 6 | Gramoxone Dual Magnum Warrant Basagran Cadre | Headline Topsin Tebuconazol Convoy Chlorothalinol | Orthene Dimilin | Boron Manganese Ascend

## Slide 25: Late-Season Insect, Weed, and Disease Ratings from 2019 Nozzle Tests with Commercial Sprayers**
 | Bulloch1 |  |  | Pierce2 |  | Worth3 | 
 | TTI- 11004 | XRC- 11004 | TDXL- 11004 | TTI- 11006 | XR- 11006 | TTI- 11006 | XRC-11006
Total # of insects (#/15 sweeps) | 8.0 | 10.0 | 9.8 | 7.8 | 7.8 | 22.8 | 20.0
Total # of weeds (#/m2) | 0 | 0 | 0 | 1.4 | 0.2 | 0 | 0
Leaf Spot (1-10) | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.2 | 1.1
White Mold (%) | 7.3 | 8.9 | 7.1 | 4.1 | 5.3 | 8.7 | 6.9
1JD4630, 90’ boom, 15” nozzle spacing, 12.0 MPH, 12 GPA, 28 PSI, 36” boom height
2JD4730, 100’ boom, 15” nozzle spacing, 11.6 MPH, 15 GPA, 18-20 PSI, 36” boom height
3JD4730, 90’ boom, 20” nozzle spacing, 12.5 MPH, 20 GPA, 42-57 PSI, 36” boom height
**No significant differences were observed between nozzle type at any location (P>0.10).

## Slide 26: 2019 Nozzle Test XRC-11004-VP
Bulloch Co.
9/9/19
115 DAP

## Slide 27: 2019 Nozzle Test TTI-11004-VP
Bulloch Co.
9/9/19
115 DAP

## Slide 28: 2019 Nozzle Test TDXL-11004-D
Bulloch Co.
9/9/19
115 DAP

## Slide 29: Peanut Yield As Influenced By Nozzle Type from 2019 Nozzle Tests with Commercial Sprayers
 | Bulloch1 |  |  | Pierce2 |  | Worth3 | 
 | TTI- 11004 | XRC- 11004 | TDXL- 11004 | TTI- 11006 | XR- 11006 | TTI- 11006 | XRC-11006
lbs/A4 | 4312 | 4338 | 4188 | 5037 | 4994 | 6588 | 6581
 | P = 0.7624 CV = 7.03 |  |  | P = 0.7596 CV = 3.63 |  | P = 0.9823 CV = 6.36 | 
1JD4630, 90’ boom, 15” nozzle spacing, 12.0 MPH, 12 GPA, 28 PSI, 36” boom height
2JD4730, 100’ boom, 15” nozzle spacing, 11.6 MPH, 15 GPA, 18-20 PSI, 36” boom height
3JD4730, 90’ boom, 20” nozzle spacing, 12.5 MPH, 20 GPA, 42-57 PSI, 36” boom height
4Adjusted to 10% moisture.

## Slide 30: Summary - 2019
Spray card analysis
  VMD50 larger with auxin nozzles (381-481 microns vs. 182-348 microns)
  Coverage better with auxin nozzles in 2/3 tests
No differences in weeds, insects, disease, and yield between nozzles were observed in large, on-farm field trials.
Pierce Co.
10/05/19

## Slide 31: Conclusions
6 on-farm, large plot replicated trials in 2018 and 2019
  + 4 site-years small-plot (weed control)
No differences between nozzle type for insects, disease, weeds, and yield.
Suggestions
  use at least 12 GPA
  good rotations
  timely applications
  grass control??
Worth Co.
09/24/19

## Slide 32: Liberty (glufosinate) - Nozzles
“Use nozzles and pressure that generate a MEDIUM to COARSE size spray droplet. NOTE: Weed control with very coarse, extremely coarse or ultra-coarse nozzles will not provide adequate coverage and will cause unsatisfactory weed control”

## Slide 33: What nozzle should I use?
What are you spraying?
  contact/systemic
label information
multiple nozzle body
  flat fat/ AIXR/”auxin”
One nozzle for everything??????
  Are you timely or late?

## Slide 34: Questions/Comments?